## Slide 1
www.Prolieve.com
Prolieve Workshop
Notes: Điều trị bằng nhiệt vi sóng qua niệu đạo (Transrethral Microwave Therapy- TUMT)
– Điều trị bằng nhiệt vi sóng dựa trên nguyên lý sử dụng bức xạ vi sóng phát ra từ một thiết bị an-ten đặt trong niệu đạo nhằm làm tăng nhiệt độ ở tuyến tiền liệt. Mô sẽ bị phá hủy khi nhiệt độ tăng lên trên ngưỡng gây độc tế bào (>45 độC).

## Slide 2: The Prolieve® System
.
.
Notes: Điều trị bằng áp nhiệt. Điều trị bằng nhiệt dựa vào việc sử dụng nhiệt do vi sóng có bước sóng 915 - 1.296 MHz phát ra từ một anten đặt bên trong niệu đạo. Sự phá hủy mô do tình trạng hoại tử cầm máu gây nên bởi nhiệt ở vùng bị đông > 44oC. Ưu điểm của phương pháp này là có thể điều trị cho bệnh nhân ngoại trú.

## Slide 3: Prolieve® Thermodilatation™
Fast, Local Anesthetic Procedure
Over 100,000 Cases Performed in the U.S.
94% Post Treatment Catheter-Free Rate
Minimal Sexual Side Effects:
  - 1% Erectile Dysfunction & Retrograde Ejaculation
  in Prolieve® Pivotal Trial (2004)
More Effective than Finasteride in Pivotal Trial (2004)
Less Discomfort & Fewer Post Treatment Catheterization
than Urologix Targis (2007 & 2010)
Over US$100 Million invested in R&D, etc.

## Slide 4
Prolieve obtained FDA – PMA Approval in Feb 2004

## Slide 5: Performed 100,000 Treatments Sep 2015
Notes: Thực hiện 100.000 điều trị đến tháng 9/2015

## Slide 6
10-Year FDA Post Market Study of Prolieve
Treated Patients with 5-Year Follow-ups
Proven Safe & Effective !
Notes: Nghiên cứu thị trường 10 năm của FDA với theo dõi 5 năm sau khi điều trị với Prolieve cho thấy tính an toàn và hiệu quả.

## Slide 7: Prolieve® ThermodilatationTM Changes the History of BPH Progression
Notes: https://vinmec-prod.s3.amazonaws.com/images/20190622_032010_311422_tuyen-tien-liet.max-800x800.jpg

## Slide 8: Prolieve® Thermodilatation™
Dilatation
Balloon
Rectal Temp
Monitor
Anchoring Balloon
Constricted Urethra
Before Prolieve®
Patent Urethra After Prolieve®
(Biological Stent WITHOUT Insertion of Foreign Bodies)
Balloon Dilatation reduces Heat Sink effect
ThermoDilatation™ employs Lower Heating Energy
Improves Patient Comfort & Fewer Catheterization
Prostate is not punctured to minimize Bleeding
Improved Coudé-Tip Catheter Design
Notes: Balloon Dilatation làm giảm hiệu ứng tản nhiệt
ThermoDilatation ™ sử dụng năng lượng làm ấm thấp hơn
Cải thiện sự thoải mái của bệnh nhân & ít đặt ống thông hơn
Tuyến tiền liệt không bị thủng để giảm thiểu chảy máu
Cải tiến thiết kế ống thông Coudé-Tip

## Slide 9: Prolieve® Thermodilatation™
ThermoDilatation ™ & TUMT thế hệ thứ 3 duy nhất được cấp bằng sáng chế 46 Fr. Dilating Balloon
Dilatation
Balloon
Rectal Temp
Monitor
Anchoring Balloon
*A 1.2 cm Microwave Antenna is Positioned At the Base of the Prostate Gland
*
*
*

## Slide 10: The Prolieve® Heating Pattern Conforms to the Shape of the Prostate Gland
Prolieve® Heating Pattern demonstrated on Liquid Crystal Sheets
*A 1.2 cm Microwave Antenna is Positioned at the Base of the Prostate Gland
Anchoring Balloon
Dilatation Balloon
Notes: Mô hình sưởi ấm Prolieve® phù hợp với hình dạng của tuyến tiền liệt

## Slide 11: Prolieve®Thermal Energy Distribution
Maximum temperatures lateral & parallel to
the urethra of a representative patient
The 3.7 cm long dilatation balloon has been
shown to leave the prostatic urethra open,
which dampens the effect of immediate
prostatic swelling post-treatment
The balloon act to protect the urethra by
maintaining the urethra wall near body
temperature 39.8°C - 40.5°C, in addition to the
cooling stream of irrigation at 30-32°C
Accurately delivers heat energy to the
prostatic tissues and to reach the temperature
threshold for achieving therapeutic effect
44.1°C - 53°C
Urology Times. Office-Based Microwave Therapy:
A First Line Treatment for BPH Advanstar Communications Inc. July 2007
URETHRA
CENTRAL PROSTRATE

## Slide 12: Ultrasound of Anchor Balloon

## Slide 13: Ultrasound of Dilatation Balloon

## Slide 18: Uroflow Before/After Treatment

## Slide 19: Prolieve® Thermal Mapping Study: MRI scan showed areas of necrosis & viable prostatic tissue
Heating pattern:
  Average peak temperatures of 51.8°C
  Average of 7mm away from prostatic urethra
Tissue necrosis was achieved in areas with sustained temperatures > 45°C
Temperatures were greater near the bladder neck and mid-gland than toward the prostatic apex
Lower temperatures were seen in the peri-urethral tissue which was preserved with viable tissue seen on MRI
Larson BT, et al. Interstitial temperature mapping during Prolieve TUMT
Urology. 2006; 68(6):1206-10.
Confidential - for Medifocus, Inc. use only

## Slide 20: Prolieve® Thermodilatation™
  Circulating water at 30 - 32°C to prevent urethral thermal injury
  A Patented 46 FG dilatation balloon reduces intra-prostatic
  blood flow & avoids heat sink effect
  Effective thermal dose delivered at lower energy level translates
  into better patient comfort during treatment
  An immediate Biological Stent allows most patients to go home
  WITHOUT a Catheter
Dilatation
Balloon
Rectal Temp
Monitor
PreOp
VCUG
“Biological Stent” postOp:
Wide Open Prostatic Urethra
Confidential - for Medifocus, Inc. use only

## Slide 21: Prolieve® Head-To-Head Trial Against Urologix Targis® Better Tolerability during Treatment
Larson BT, et al. Interstitial temperature mapping during Prolieve TUMT
Urology. 2006; 68(6):1206-10.

## Slide 22: Patient Post Treatment Catheter-Free Rate: 94% of Prolieve® vs. 21% of Urologix Targis®
Shore ND et al.: A Controlled, Randomized, Head-to-Head Comparison of
Prolieve® vs. Targis® for BPH. J Endourology. 24(9): 1469-1475 (2010).
Notes: Tỷ lệ bệnh nhân sau điều trị không dùng ống thông: 94% của Prolieve® so với 21% của Urologix Targis®

## Slide 23: Prolieve® Thermodilatation™ 120-Month Post Market Study
Objective: To evaluate the long-term safety and effectiveness of Prolieve®
in treating BPH with 5-Year Follow-Ups
Patient Characteristics:
  Mean Age = 65.01 (±8.75)
  Mean Prostate Size = 41.45 grams (Range = 19 to 80 grams)
  Prostatic Urethra Length between 1.2 and 5.5 cm
  Peak urine flow rate ˂12ml/sec on voided volume of >125ml
  AUA symptom score ≥9
Exclusion Criteria: Obstructive Median Lobe of the prostate with a
“Ball-Valve” Configuration were excluded among other Criteria
Confidential - for Medifocus, Inc. use only
Notes: Mục tiêu: để đánh giá tính an toàn và hiệu quả của Prolieve trong điều trị BPH với 5 năm theo dõi.
Đặc điểm bệnh nhân:
Tuổi trung bình: 65.01 (± 8,75)
Kích thước tuyến tiền liệt trung bình = 41,45 gam (Phạm vi = 19 đến 80 gam)
Chiều dài niệu đạo tuyến tiền liệt từ 1,2 đến 5,5 cm
Tốc độ dòng nước tiểu cao nhất ˂12ml / giây trên thể tích vô hiệu> 125ml
Điểm triệu chứng AUA ≥9
Tiêu chí loại trừ: Thùy trung tuyến bị tắc nghẽn của tuyến tiền liệt có cấu hình "Van bi" đã bị loại trừ trong số các Tiêu chí khác

## Slide 24: Catheter-Free Rate: 85% of Patients Did Not Require Catheterization after Prolieve®
Chart: 
| No | Yes
No. of Patient | 187 | 33
N=220
Notes: Tỉ lệ không cần dùng ống thông: 85% bênh nhân không cần ống thông sau khi sử dụng Prolieve

## Slide 25: Significant Change from Baseline in AUA Symptom Score
*
*
*
*
*
*
Chart: AUA Score (Mean ± Std)
| Baseline (N=220) | Week 2 (N=220) | Month 3 (N=215) | Year 1 (N=195) | Year 2 (N=156) | Year 3 (N=134) | Year 4 (N=100) | Year 5 (N=94)
+Std | 26.03 | 22.47 | 16.53 | 18.54 | 18.93 | 19.04 | 18.66 | 19.56
Mean Value | 20.12 | 15.5 | 10.62 | 12.02 | 12.25 | 12.48 | 12.35 | 12.86
-Std | 14.21 | 8.53 | 4.71 | 5.5 | 5.57 | 5.92 | 6.04 | 6.16
Chart: Change (Mean ± Std)
| Baseline (N=220) | Week 2 (N=220) | Month 3 (N=215) | Year 1 (N=195) | Year 2 (N=156) | Year 3 (N=134) | Year 4 (N=100) | Year 5 (N=94)
+Std | 0 | 12.16 | 16.59 | 14.93 | 14.69 | 14.54 | 13.85 | 14.21
Mean Change | 0 | 4.61 | 9.49 | 7.75 | 7.46 | 7.17 | 6.83 | 6.58
-Std | 0 | -2.94 | 2.39 | 0.57 | 0.23 | -0.2 | -0.19 | -1.05
*
*
*
*
*
*
*
* Statistically significant change from Baseline (p<0.001)

## Slide 26: Significant Change from Baseline in QOL Scores
Chart: QOL Value (Mean ± Std)
| Baseline (N=220) | Week 2 (N=220) | Month 3 (N=215) | Year 1 (N=195) | Year 2 (N=156) | Year 3 (N=134) | Year 4 (N=100) | Year 5 (N=94)
+Std | 26.46 | 23.27 | 20.57 | 21.23 | 21.03 | 21.14 | 21.82 | 21.27
Mean Value | 21.98 | 17.8 | 15.35 | 15.73 | 15.92 | 16 | 16.6 | 16.47
-Std | 17.5 | 12.33 | 10.13 | 10.23 | 10.81 | 10.86 | 11.38 | 11.67
Chart: Change (Mean ± Std)
| Baseline (N=220) | Week 2 (N=220) | Month 3 (N=215) | Year 1 (N=195) | Year 2 (N=156) | Year 3 (N=134) | Year 4 (N=100) | Year 5 (N=94)
+Std | 0 | 9.66 | 11.99 | 11.85 | 11.74 | 11.47 | 10.72 | 10.79
Mean Value | 0 | 4.17 | 6.63 | 6.08 | 5.93 | 6.08 | 5.31 | 5.39
-Std | 0 | -1.32 | 1.27 | 0.31 | 0.12 | 0.69 | -0.1 | -0.01
* Statistically significant change from Baseline (p<0.05)
*

## Slide 27: No Change from Baseline in Serum PSA
Chart: PSA (Mean ± Std)
| Baseline (N=220) | Week 2 (N=220) | Month 3 (N=215) | Year 1 (N=195) | Year 2 (N=156) | Year 3 (N=134) | Year 4 (N=100) | Year 5 (N=94)
+Std | 4.28 | 7.37 | 5.25 | 4.73 | 6.3 | 8.43 | 7.69 | 6.01
Mean Value | 2.23 | 3.52 | 2.35 | 2.45 | 2.56 | 2.73 | 2.49 | 2.44
-Std | 0.18 | -0.33 | -0.55 | 0.17 | -1.18 | -2.97 | -2.71 | -1.13
Chart: Change (Mean ± Std)
| Baseline (N=220) | Week 2 (N=220) | Month 3 (N=215) | Year 1 (N=195) | Year 2 (N=156) | Year 3 (N=134) | Year 4 (N=100) | Year 5 (N=94)
+Std | 0 | 1.79 | 2.33 | 1.45 | 3.27 | 4.96 | 4.93 | 3.22
Mean Change | 0 | -1.3 | -0.12 | -0.17 | -0.34 | -0.63 | -0.39 | -0.13
-Std | 0 | -4.39 | -2.57 | -1.79 | -3.95 | -6.22 | -5.71 | -3.48
P<0.001
P=0.467
P=0.147
P=0.238
P=0.200
P=0.468
P=0.705
* No Statistically significant changes from Baseline (p>0.05)

## Slide 28: Significant Change in Peak Flow Rate (Qmax)
Chart: Qmax mL/sec (Mean ± Std)
| Baseline (N=220) | Year 1 (N=185) | Year 2 (N=150) | Year 3 (N=131) | Year 4 (N=99) | Year 5 (N=89)
+Std | 11.11 | 17.21 | 17.2 | 19.16 | 20.08 | 21.12
Mean Value | 8.55 | 11.2 | 11.7 | 12.38 | 12.41 | 13.04
-Std | 5.99 | 5.19 | 6.2 | 5.6 | 4.74 | 4.96
Chart: Qmax Change (Mean ± Std)
| Baseline (N=220) | Year 1 (N=185) | Year 2 (N=150) | Year 3 (N=131) | Year 4 (N=99) | Year 5 (N=89)
+Std | 0 | 8.65 | 8.15 | 10.94 | 12.25 | 13.36
Mean Change | 0 | 2.66 | 2.56 | 3.8 | 4.17 | 4.89
-Std | 0 | -3.33 | -3.03 | -3.34 | -3.91 | -3.58
* Statistically significant change from Baseline (p<0.05)

## Slide 29: Significant Change in Peak Flow Rate (Qmax)
Chart: Qmax mL/sec (Mean ± Std)
| Baseline (N=220) | Year 1 (N=185) | Year 2 (N=150) | Year 3 (N=131) | Year 4 (N=99) | Year 5 (N=89)
+Std | 11.11 | 17.21 | 17.2 | 19.16 | 20.08 | 21.12
Mean Value | 8.55 | 11.2 | 11.7 | 12.38 | 12.41 | 13.04
-Std | 5.99 | 5.19 | 6.2 | 5.6 | 4.74 | 4.96
Chart: Qmax Change (Mean ± Std)
| Baseline (N=220) | Year 1 (N=185) | Year 2 (N=150) | Year 3 (N=131) | Year 4 (N=99) | Year 5 (N=89)
+Std | 0 | 8.65 | 8.15 | 10.94 | 12.25 | 13.36
Mean Change | 0 | 2.66 | 2.56 | 3.8 | 4.17 | 4.89
-Std | 0 | -3.33 | -3.03 | -3.34 | -3.91 | -3.58
* Statistically significant change from Baseline (p<0.05)

## Slide 30: Conclusion
Fast, Local Anesthetic Procedure
Over 100,000 Cases Performed in the U.S.
85% Post-Treatment Catheter-Free Rate (94% in Another Prolieve® Trial)
Minimal Sexual Side Effects
  Erectile Dysfunction: 2.0 per 100 person-years
  Retrograde Ejaculation: 1.8 per 100 person-years
  (1% ED & RE in Prolieve® Pivotal Trial)
Improvement of Mean AUA Symptom Score
  Baseline = 20.12 vs. Year 5 = 12.86

## Slide 31: Conclusion (Cont’d)
Improvement of Peak Flow Rate
  Baseline = 8.55 mL/sec vs. Year 5 = 13.04 mL/sec
Improvement of Quality of Life Score by 25%
  Baseline = 22 vs. Year 5 = 16.5
Stabilization of Serum PSA
  Baseline = 2.23 ng/dL vs. Year 5 = 2.44 ng/dL
Stabilization of BPH Symptoms
  78% reported No Progression at Year 5

## Slide 32: Take Home Messages
If Left Untreated, many men with Symptomatic BPH will risk
  - Progression of LUTS; - Diminished Qmax & QOL
  - Rise in PSA; - Increase in Prostate Volume
The Side Effects of Surgery or Drug Therapy can be Significant
In this Longitudinal Study, Prolieve® ThermoDilatation™ is shown to
Lower these Risks & Change the Natural History of BPH Progression
Prolieve® is a Proven Safe & Effective Treatment Option
For Symptomatic BPH patients .

## Slide 33
Thank you !